## Slide 1
Constrained Application Protocol(CoAP)
Made by Keyhan Masoudi
Sharif University of Technology Dr.Amin Foshati

## Slide 2
What is CoAP
The Constrained Application Protocol (CoAP) is a lightweight web transfer protocol designed for constrained devices and networks. It is optimized for applications in the Internet of Things (IoT), ensuring low power consumption and efficient bandwidth usage.

## Slide 3
Purpose of Development CoAP
Why CoAP?
Efficient communication in low-bandwidth, high-latency networks.
Low resource consumption for constrained devices.
Easy integration with web technologies.
Easily adaptable to various devices across IoT applications
Send information to multiple devices simultaneously.

## Slide 4
Applicatioin Layer Connections
Optimized RESTful architecture
Supports block-wise transfer
Supports optional secure communication through DTLS.
Supports resource discovery
Caching repeated data

## Slide 5
Communication Type and Encoding
1
Serial Communication
CoAP messages are transmitted serially.
2
Encoding
Compact binary format to minimize overhead.
3
Signal Production
Utilizes UDP packets for asynchronous, low-latency communication.

## Slide 6
Device Connectivity
Multi-Device Capability
Allows multiple devices to communicate with a single server.

## Slide 7
Addressing and Routing
1
IP Addressing
To identify and communicate with devices
Supports unicast (1-to-1 and 1-to-many)
2
No Routing Features
Routing is managed by underlying network protocols (e.g., RPL).

## Slide 8
Data Flow Management
1
Flow Control
Managed by message acknowledgment.
3
Retransmission Mechanism
Ensures data reliability in case of packet loss.
2
Message Deduplication
Ignore duplicate messages

## Slide 9
Error Detection
1
Data Link Layer
Integrity is maintained through UDP checksums.
2
Higher Layers
Application-level errors are identified through response codes(e.g,4.04).
Error Correction
CoAP primarily focuses on error detection and retransmission rather than complex error correction techniques.

## Slide 10
Message Types and Formats
Version
Type
Token Length
Code
Message ID
Options
Payload
CoAP uses four message types:
Confirmable.
Non-confirmable.
Acknowledgment.
Reset.

## Slide 11
Thanks for your attention
Under the guidance of Dr.Foshati
Interface Circuits Design
Fall 2024

## Slide 12
Reference
https://www.geeksforgeeks.org/constrained-application-protocol-coap/
https://devopedia.org/constrained-application-protocol
https://core-wg.github.io/new-block/draft-ietf-core-new-block.html
http://rfc-editor.org/rfc/rfc7252.html
https://coap.space/\