## Slide 1
PATA: A Look Back at Parallel ATA
Parallel Advanced Technology Attachment (PATA) was a standard for connecting storage devices to motherboards, such as hard drives and optical discs.
by Nika Ghaderi
1

## Slide 2
Table of contents
PATA's History and Evolution
Sample Usage
PATA's Architecture and Signaling
PATA's Architecture and Signaling (cont'd)
PATA's Architecture and Signalingv (cont'd)
PATA's Architecture and Signaling (cont'd)
PATA's Architecture and Signaling (cont'd)
PATA Dual-Drive Configurations
PATA vs SATA
PATA's Legacy
Thank you for your attention!
2

## Slide 3
PATA's History and Evolution
Early Days
Invented by Western Digital in 1986, originally called Integrated Drive Electronics (IDE).
Speed up to 16 MB/s
Evolution
ATA 1,2,4,6 and 7
Speed up to 133 MB/s
Support for CD-ROMs and other devices
3

## Slide 4
Sample Usage
4

## Slide 5
PATA's Architecture and Signaling
1
Transaction Layer
Manages command execution, data transfers, and device coordination.
2
Data Link Layer
Manages data framing, error detection, and flow control between host and device.
3
Physical Layer
Defines electrical and mechanical characteristics, including signaling, cabling, connectors, and timing.
5

## Slide 6
PATA's Architecture and Signaling (cont'd)
Physical Layer
Signaling
Single-ended signaling (not differential).
Voltage levels: 5V (older) or 3.3V (newer).
Susceptible to noise and crosstalk.
Cabling
40-pin ribbon cable: 16 data lines + control/ground.
80-conductor cable: Reduced crosstalk (ATA/66+).
Max length: 18 inches (45 cm).
Connectors
40-pin IDC connector.
Master/Slave configuration via jumpers.
Timing
Synchronized using strobe signals (DIOR#, DIOW#).
Data rates: 16.6 MB/s (ATA-1) to 133 MB/s (ATA-7).
6

## Slide 7
PATA's Architecture and Signalingv (cont'd)
Physical Layer
7

## Slide 8
PATA's Architecture and Signaling (cont'd)
Data Link Layer
Data Framing
16-bit parallel transfers.
Block transfers (512-byte sectors).
Error Detection
CRC for data integrity.
Optional parity checking.
Flow Control
IORDY signal for pausing host.
Protocol Commands
Basic commands: Identify Device, Read/Write Sector
8

## Slide 9
PATA's Architecture and Signaling (cont'd)
Transaction Layer
Command Execution
ATA commands via Task File Registers.
Parameters: Sector count, LBA (3), operation type.
Data Transfer Modes
PIO: CPU-managed (slower).
DMA: Direct to memory (faster).
UDMA: Enhanced DMA with CRC.
Task File Registers
Configure commands (e.g., Read Sector).
Master/Slave Arbitration
Manages communication for shared cables.
9

## Slide 10
PATA Dual-Drive Configurations
Device Designation
Device 0 (Master) and Device 1 (Slave). (No priority and dependance)
Share the same bus.
Only one controller responds to commands at a time. (DRV)
Jumper Settings
Device 0/1 or Cable Select (CS).
CS: Automatically assigns device based on cable position.
Default: Usually Cable Select (if no jumpers are set).
10

## Slide 11
PATA vs SATA
Transfer Speed: SATA > PATA.
1
Cable Length: SATA (1m) > PATA (46cm).
2
Performance: SATA supports hot-swapping; PATA does not.
3
Compatibility: SATA supports forward/backward compatibility.
4
Versatility: PATA connects 2 devices per cable; SATA has 2 ports.
5
11

## Slide 12
PATA's Legacy
PATA played a crucial role in the development of computer storage technology, paving the way for faster and more versatile interfaces like SATA. While PATA is no longer widely used, its impact on the evolution of computer hardware remains significant.
12

## Slide 13
Thank you for your attention!
Under the guidance of Dr. Foshati
Interface Circuits Design
Sharif University of Technology
Fall 2024
13